Brief Overview of ESP32-CAM
- The ESP32-CAM is a compact camera module based on the ESP32 microcontroller, equipped with an OV2640 camera and onboard TF card slot.
- Its notable features include a powerful 4MB PSRAM, allowing for image buffering during video streaming without compromising the ESP32's stability.
- With WiFi and Bluetooth support, the ESP32-CAM facilitates wireless communication and integration into IoT applications.
WiFi Capabilities and Camera Specifications:
- The ESP32-CAM's WiFi capabilities, supported by the ESP-32S module, enable versatile applications such as real-time video streaming, image uploads, and remote control.
- The OV2640 camera with flash delivers high-quality images in JPEG format and supports other formats like BMP and GRAYSCALE.
- The module's ability to support up to 4GB TF cards for data storage further enhances its utility.
Websockets Integration:
Websockets provide a robust communication protocol for real-time, bidirectional communication between the ESP32-CAM and external devices (Control server), making it an ideal choice for surveillance and control applications.
The integration involves three key channels:
1. Camera Streaming Channel:
  1. The ESP32-CAM streams video in real-time over a websocket connection.
  2. Clients can receive and display the live camera feed on web applications or other compatible platforms.
2. Rover Control Channel:
  1. Websockets facilitate remote control of the surveillance rover by enabling bidirectional communication.
  2. Commands from a control interface, such as a web application, are sent to the ESP32-CAM, allowing users to navigate the rover.
3. Sensor Data Channel:
  1. Websockets enable the transmission of sensor data from the ESP32-CAM to a monitoring interface.
  2. Information such as metal detector readings or environmental data collected by sensors on the rover can be relayed in real-time.

Control Server
- The server, serving as the control server, is hosted on my laptop.
- All three channels, including camera streaming, rover control, and sensor data, are connected to the control server.
- In this setup, the control server plays a crucial role in collecting and processing data transmitted by the rover, encompassing information from the camera, sensors, trajectory, and GPS.
- The collected data is then transformed into a user-friendly format and displayed on the server page, providing an intuitive user interface.
- Moreover, the control server serves as a command center, allowing users to maneuver and command the rover efficiently.
- It acts as a central hub where data from various sources is stored, crunched, and presented for user monitoring and control.
WebSocket Server Architecture:
The architecture of the WebSocket system involving the ESP32-CAM and my laptop as the server comprises the following key components:
1. ESP32-CAM Module (WebSocket Client):
  1. Operates as a WebSocket client, connecting to the WebSocket server on my laptop.
  2. Manages bidirectional communication, handling both incoming and outgoing messages with the server.
2. WebSocket Library:
  1. Utilizes a WebSocket library compatible with the ESP32 framework, facilitating communication protocols.
  2. Ensures efficient and secure data exchange between the ESP32-CAM (client) and the server.
3. Communication Protocols:
  1. Adopts the WebSocket protocol (RFC 6455) for bidirectional communication between the ESP32-CAM (client) and the server.
  2. Implements specific messaging protocols for each channel, ensuring organized and secure data transfer.
4. Server (My Laptop):
  1. Functions as the WebSocket server, managing multiple WebSocket clients, including the ESP32-CAM.
  2. Handles communication channels and processes data received from the ESP32-CAM, such as camera streaming, rover control, and sensor data.
5. Client Interfaces (ESP32-CAM):
  1. The ESP32-CAM serves as a WebSocket client, connecting to the WebSocket server running on my laptop.
  2. Allows clients, like external devices or web applications, to subscribe to various channels based on functionality (e.g., camera streaming, rover control, sensor data).
In this configuration, my laptop operates as the WebSocket server, managing communication with the ESP32-CAM acting as the WebSocket client. The bidirectional flow of data ensures seamless integration and control between the server and the ESP32-CAM, providing a flexible and responsive framework for real-world applications such as surveillance rovers and metal detectors.

Working Principle of Neo-6M GPS Module:
The Neo-6M GPS module is a compact and affordable Global Positioning System (GPS) receiver designed for accurate location tracking. It operates on the principles of trilateration, utilizing signals from multiple satellites to determine its precise location on Earth. Here's an overview of its working principle:
1. Satellite Signal Reception:
  1. The Neo-6M module relies on signals transmitted by a network of GPS satellites orbiting the Earth.
  2. A minimum of four satellite signals is needed for accurate position triangulation.
2. Trilateration Calculation:
  1. The module calculates its distance from each satellite based on the time it takes for the signals to reach the receiver.
  2. By combining these distances, the Neo-6M determines its 3D position (latitude, longitude, and altitude) using a process known as trilateration.
3. Data Processing:
  1. The module processes the received satellite signals and extracts essential information such as location, time, and satellite data.
4. Output:
  1. The Neo-6M outputs the acquired GPS data in standard NMEA (National Marine Electronics Association) sentences, a common protocol for GPS data communication.
      5. Data Transmission to Control Server
    - The ESP32-CAM dispatches formatted GPS data through the dedicated sensor data channel on the WebSocket connection.
      6.Control Server Processing:
    - The control server, hosted on my laptop, assumes the role of an omniscient overseer, meticulously processing incoming GPS data streams.
    - This processing stage intelligently intertwines location specifics with mapping services or other applications, presenting the culmination in a user-friendly interface on the control server. Here, real-time and actionable location insights are offered to the user.